## Slide 1: Wireless Tape Measurer
Veronika Sermeno Pon
TECHIN 514
Final Project
Github Repo: https://github.com/vpon-lab/514-Final-Project

## Slide 2: Measuring alone
Problem to Solve:
Wanting to measure bedroom space on your own with out another person’s assistance.
Mitigate sag from a physical tape measurer.

## Slide 3: Measuring alone
A proposed Solution:
Wireless tape measurement
2-piece system to measure from point A to point B
Notes: Insert picture once prints are done

## Slide 4: System Architecture

## Slide 5: Sensing + Display Device
XIAO ESP32C3
Time of Flight Laser Sensor
X27 Stepper Motor
OLED Display
Power On/Off Switch
“Tare” Button
Sensor Device
Display Device
Due to multiple ESP32C3 Battery pad mishaps, this is not battery powered for cautionary measures
Notes: Insert picture once prints are done

## Slide 6: Signal Processing
Moving average filter, numbers were the same at the first decimal place before filter.
Accuracy:
  ±0.01 ft
  ±3mm
  Degrades with distance
Display Device shows sensor jumping between measurements – from table to ceiling

## Slide 7: Battery Considerations – Sensing device
3.7V Lipo or Li-Ion Battery
Compact easy to design with in enclosure and long lasting
Based on 2hrs/day of use

## Slide 8: Appendix
Budget Summary
Anything with “$0” was free in the Maker Space

## Slide 9: Future Work
Sensor Calibration to get rid of cross-talk from clear acrylic window.
Sensor Calibration to find max capable distance based on Bluetooth connection compatibility
Develop a more ergonomic and detachable/portable enclosure(s)
Proper PCB design for easy battery connection to Display device.

## Slide 10: Appendix
Power Model

## Slide 11: Appendix
Budget Summary
Anything with “$0” was free in the Maker Space

## Slide 12: Appendix
Enclosure Design
Due to multiple ESP32C3 Battery pad mishaps, this is not battery powered for cautionary measures
Sensor Device
Display Device